## Slide 1: Wireless Sensor Network Health Diagnostic
David Rogers, Stu Andrzejewski,
Kelly Desmond, Brad Garrod
Design Team 2

## Slide 2
Problem Statement
In order to ensure a properly functioning wireless sensor network, the Air Force needs a network health diagnostic tool that is easy to use, accurate and reliable.

## Slide 3
Sensors outnumber people

## Slide 4
Project Goals
SET GOALS.
MAKE PLAN.
REACH GOALS.
GET TO WORK.
STICK TO IT.
Configure a state of the art wireless sensor network.
Be able to collect the data from the network.
Design and Develop a software package for displaying sensor data in real time.
Develop algorithms that help analyze the correlations between network metrics and node failure.

## Slide 5: Specifications & Requirements
Must Be Satisfied
  Fully Configured Wireless Sensor Network
  Low Power Sensor Nodes
  Reliable Communication with and within the Network
  Accurate Sensor Node Measurements
Increases Design Desirability
  Simple Network Configuration
  Development of Graphical User Interface

## Slide 6: Final Design
Hardware
  Powercast P2110-Eval-01
Software
  Graphical User Interface (modified MVC)
    Controller (pySerial)
    Model
    View (wxPython, Matplotlib)
  Metric Analysis Algorithms
    Short Term
    Long term
    Zero Value

## Slide 7: Final Design
Hardware
  Powercast P2110-Eval-01
Software
  Graphical User Interface (modified MVC)
    Controller (pySerial)
    Model
    View (wxPython, Matplotlib)
  Metric Analysis Algorithms
    Short Term
    Long term
    Zero Value

## Slide 8: Powercast P2110-EVAL-01 Development Kit
Goal #1:
  Configure a state of the art wireless sensor network
Power and Data Transmitter
(2) P2110 Evaluation Board
(2) Patch Antennas
(2) Dipole Antennas
(2) Wireless Sensor Board
Microchip 16-bit XLP Development Board
Microchip MRF24J40 PICtail
PICkit Programmer/Debugger

## Slide 9: 915 MHz Powercaster Transmitter
915MHz ISM band
Transmits power and data
  Outputs 3 watts
  Transmits transmitter ID
8dBi integrated antenna
Capable of wall or table mount
Beam Pattern-60° width, 60 ° height
Wide temperature range
Ability to power multiple receivers

## Slide 10: Microchip 16-Bit XLP Development Board
Contains a PIC24FK embedded MCU
2.4 GHz Radio Module
Configured for up to eight sensor nodes
Maintains time counters for each node
Configuration selection jumpers to disable board components
USB connectivity
Two user-defined LEDs
Built-in capability for separately measuring microcontroller and component current consumption

## Slide 11: P2110 Evaluation Board & Antennas
P2110 Evaluation Board
  P2110 Powerharveter
    Converts RF energy to regulated DC power
  Charge/Power Management
  I/O for interface to MCU
Antennas
  Dipole (360° Reception Pattern – Omni-Directional)
  Patch (120° Reception Pattern - Directional)

## Slide 12: Wireless Sensor Boards
Node ID Selection
Transmitter ID Capture
Sensors
  Temperature
  Light
  Humidity
  External Sensor Port
RSSI Calculation
PIC Embedded MCU
2.4 GHz Radio Module
Sensors

## Slide 13: Wireless Sensor Network Flowchart

## Slide 14: Hardware Testing
Test Name | Sensor Node Position (Angle in Relation to Transmitter) |  | Transmitter (Height & Distance from Sensor Nodes) |  | Sensor Status (Jumper Pins Pulled On Certain Sensors) |  |  | Test Time
 | Height | Width | Distance | Height | Temperature | Light | Humidity | 
Sample2-3 | 3.97° | 0° | 3ft | 2.5 inches | Not Active | Active | Active | 30 mins
Sample2-4 | 3.97° | 0° | 3ft | 2.5 inches | Active | Not Active | Active | 30 mins
Sample2-5 | 3.97° | 0° | 3ft | 2.5 inches | Not Active | Active | Not Active | 30 mins
Sample2-6 | 3.97° | 0° | 3ft | 2.5 inches | Not Active | Not Active | Not Active | 30 mins
Sample2-7 | 15.25° | 0° | 8ft | 4ft | Active | Active | Active | 45 mins
Sample2-8 | 0° | 0° | 2ft | 0ft | Active | Active | Active | 2 hr
Sample2-9 | 0° | 48.5° | 2.67ft | 0ft | Active | Active | Active | 30 mins

## Slide 15: Hardware Testing

## Slide 16: Final Design
Hardware
  Powercast P2110-Eval-01
Software
  Graphical User Interface (modified MVC)
    Controller (pySerial)
    Model
    View (wxPython, Matplotlib)
  Metric Analysis Algorithms
    Short Term
    Long term
    Zero Value

## Slide 17: Graphical User Interface - MVC
Model-View-Controller (MVC)
Design Pattern
Goal #2:
  Be able to collect the data from the network.
Goal #3:
  Design and develop a software package for displaying sensor data in real time.

## Slide 18: Controller
Launch the application in a specific mode
  Demo or Real-time
Main Functions:
  Collect data from the network over USB (pySerial)
  Manipulates data into individual packets
Notes: A controller can send commands to the model to update the model's state (e.g., editing a document). It can also send commands to its associated view to change the view's presentation of the model (e.g., by scrolling through a document).

## Slide 19: Real-time Data Close-Up

## Slide 20: Model
Manipulates and maintains data packets sent from controller
Application programming interface (API)
  Acts like a database
Allows for metric analysis integration
Able to manage streaming data in real-time efficiently
Notes: A model notifies its associated views and controllers when there has been a change in its state. This notification allows the views to produce updated output, and the controllers to change the available set of commands.

## Slide 21: View
Run concurrently on its own thread
  Robust to crashes
Leverages multiple libraries
  wxPython
  Matplotlib
Features:
  Saving plots
  Manual & Auto scaling
  Display multiple nodes simultaneously
  Switch between metrics
Notes: A view requests information from the model that it needs for generating an output representation to the user

## Slide 22: Minimum Viable Product
The application running in demo mode with data from sample2-3

## Slide 23: Final Design
Hardware
  Powercast P2110-Eval-01
Software
  Graphical User Interface (modified MVC)
    Controller (pySerial)
    Model
    View (wxPython, Matplotlib)
  Metric Analysis Algorithms
    Short Term
    Long term
    Zero Value

## Slide 24: Metrics Analysis Approach
Goal #4:
  Develop algorithms that help analyze the correlations between network metrics and node failure.
Function approach to minimize time
Parse through packet data
  Grab appropriate data
  Filter into readable data sets
  Convert into comma separated value file
Read and analyze data
  Plot graphs
  Calculate averages
  Determine thresholds

## Slide 25: Metric Analysis Results

## Slide 26: Short Term Failure
Primarily external sensors
Data against average for past 4 samples

## Slide 27: Long Term Failure
Primarily internal sensors
Data against average for large chunk of past data

## Slide 28: Zero Value Failure
Can be used for any sensor
Looks for unexpected zeros in data

## Slide 29: Final Design
Hardware
  Powercast P2110-Eval-01
Software
  Graphical User Interface (modified MVC)
    Controller (pySerial)
    Model
    View (wxPython, Matplotlib)
  Metric Analysis Algorithms
    Short Term
    Long term
    Zero Value

## Slide 30: Budget
Product | Cost
Powercast P2110 EVAL-01 Development Kit | $1250
Total | $1250

## Slide 31
http://www.egr.msu.edu/classes/ece480/capstone/fall13/group02/